## Slide 1: Exercise 2.10
In the following problems, the data table contains bits that represent the opcode of an instruction. You will be asked to interpret the bits as MIPS instructions into assembly code and determine what format of MIPS instruction the bits represent.
2.10.1 [5] <2.5> For the binary entries above, what instruction do they represent?
2.10.2 [5] <2.5> What type (I-type, R-type, J-type) instruction do the binary
entries above represent?
2.10.3 [5] <2.4, 2.5> If the binary entries above were data bits, what number would they represent in hexadecimal?
a. | 0000 0010 0001 0000 1000 0000 0010 0000
b. | 0000 0001 0100 1011 0100 1000 0010 0010

## Slide 2: Exercise 2.10 (cont.)
In the following problems, the data table contains MIPS instructions. You will be asked to translate the entries into the bits of the opcode and determine the MIPS instruction format.
2.10.4 [5] <2.4, 2.5> For the instructions above, show the binary then hexadecimal representation of these instructions.
2.10.5 [5] <2.5> What type (I-type, R-type, J-type) instruction do the instructions above represent?
2.10.6 [5] <2.5> What is the binary then hexadecimal representation of the opcode, Rs, and Rt fields in this instruction? For R-type instructions, what is the hexadecimal representation of the Rd and funct fields? For I-type instructions, what is the hexadecimal representation of the immediate field?
a. | addi $t0, $t0, 0
b. | sw $t1, 32($t2)