## Slide 1: Exercise 2.13
In the following problems, the data table contains the values for registers $t0 and $t1. You will be asked to perform several MIPS logical operations on these registers.
2.13.1 [5] <2.6> For the lines above, what is the value of $t2 for the following sequence of instructions?
  sll $t2, $t0, 4
  or $t2, $t2, $t1
2.13.2 [5] <2.6> For the values in the table above, what is the value of $t2 for the following sequence of instructions?
sll $t2, $t0, 4
andi $t2, $t2, –1
2.13.3 [5] <2.6> For the lines above, what is the value of $t2 for the following sequence of instructions?
srl $t2, $t0, 3
andi $t2, $t2, 0xFFEF
a. | $t0 = 0xAAAAAAAA, $t1 = 0x12345678
b. | $t0 = 0xF00DD00D, $t1 = 0x11111111

## Slide 2: Exercise 2.13 (cont.)
In the following exercise, the data table contains various MIPS logical operations. You will be asked to find the result of these operations given values for registers $t0 and $t1.
2.13.4 [5] <2.6> Assume that $t0 = 0x0000A5A5 and $t1 = 00005A5A. What is the value of $t2 after the two instructions in the table?
2.13.5 [5] <2.6> Assume that $t0 = 0xA5A50000 and $t1 = A5A50000. What is the value of $t2 after the two instructions in the table?
2.13.6 [5] <2.6> Assume that $t0 = 0xA5A5FFFF and $t1 = A5A5FFFF. What is the value of $t2 after the two instructions in the table?
a. | sll $t2, $t0, 1 andi $t2, $t2, –1
b. | andi $t2, $t1, 0x00F0 srl $t2, 2