## Slide 1: Exercise 2.15
For these problems, the table holds some logical operations that are not included in the MIPS instruction set. How can these instructions be implemented?
2.15.1 [5] <2.6> The logical instructions above are not included in the MIPS instruction set, but are described above. If the value of $t2 = 0x00FFA5A5 and the value of $t3 = 0xFFFF003C, what is the result in $t1?
2.15.2 [10] <2.6> The logical instructions above are not included in the MIPS instruction set, but can be synthesized using one or more MIPS assembly instructions. Provide a minimal set of MIPS instructions that may be used in place of the instructions in the table above.
2.15.3 [5] <2.6> For your sequence of instructions in 2.15.2, show the bit-level representation of each instruction.
a. | not $t1, $t2 // bit-wise invert
b. | orn $t1, $t2, $t3 // bit-wise OR of $t2, !$t3

## Slide 2: Exercise 2.15 (cont.)
Various C-level logical statements are shown in the table below. In this exercise, you will be asked to evaluate the statements and implement these C statements using MIPS assembly instructions.
2.15.4 [5] <2.6> The table above shows different C statements that use logical operators. If the memory location at C[0] contains the integer values 0x00001234, and the initial integer values of A and B are 0x00000000 and 0x00002222, what is the result value of A?
2.15.5 [5] <2.6> For the C statements in the table above, write a minimal sequence of MIPS assembly instructions that does the identical operation. Assume $t1 = A, $t2 = B, and $s1 is the base address of C.
2.15.6 [5] <2.6> For your sequence of instructions in 2.15.5, show the bit-level representation of each instruction.
a. | A = B ¦ !A;
b. | A = C[0] << 4;