## Slide 1: Exercise 2.18
For these problems, the table holds some C code. You will be asked to evaluate these C code statements in MIPS assembly code.
2.18.1 [5] <2.7> For the table above, draw a control-flow graph of the C code.
2.18.2 [5] <2.7> For the table above, translate the C code to MIPS assembly code. Use a minimum number of instructions. Assume that the values of a, b, i, and j are in registers $s0, $s1, $t0, and $t1, respectively. Also, assume that register $s2 holds the base address of the array D.
2.18.3 [5] <2.7> How many MIPS instructions does it take to implement the C code? If the variables a and b are initialized to 10 and 1 and all elements of D are initially 0, what is the total number of MIPS instructions that is executed to complete the loop?
a. | for(i=0; i<a; i++) a += b;
b. | for(i=0; i<a; i++) for(j=0; j<b; j++) D[4*j] = i + j;

## Slide 2: Exercise 2.18 (cont.)
For these problems, the table holds MIPS assembly code fragments. You will be asked to evaluate each of the code fragments, familiarizing you with the different MIPS branch instructions.
a. | addi $t1, $0, 50 LOOP: lw $s1, 0($s0) add $s2, $s2, $s1 lw $s1, 4($s0) add $s2, $s2, $s1 addi $s0, $s0, 8 subi $t1, $t1, 1 bne $t1, $0, LOOP
b. | addi $t1, $0, $0 LOOP: lw $s1, 0($s0) add $s2, $s2, $s1 addi $s0, $s0, 4 addi $t1, $t1, 1 slti $t2, $t1, 100 bne $t2, $s0, LOOP
2.18.4 [5] <2.7> What is the total number of MIPS instructions executed?
2.18.5 [5] <2.7> Translate the loops above into C. Assume that the C-level integer i is held in register $t1, $s2 holds the C-level integer called result, and $s0 holds the base address of the integer MemArray.
2.18.6 [5] <2.7> Rewrite the loop to reduce the number of MIPS instructions executed.

## Slide 3: Exercise 2.18 (cont.)
Home work: The Class is divided into groups (Given Student list). Upper half do the part 1 (2.18.1-2.18.3) and Lower half do the part 2 (2.18.4-2.18-6).
Sent by Email with file attched: “Name-Student code” as file name.
Deadline: til Midnight Tuesday (22nd March 2016)