## Slide 1: CPUs
Input and output.
Supervisor mode, exceptions, traps.
Co-processors.

## Slide 2: I/O devices
Usually includes some non-digital component.
Typical digital interface to CPU:
CPU
status
reg
data
reg
mechanism

## Slide 3: Application: 8251 UART
Universal asynchronous receiver transmitter (UART) : provides serial communication.
8251 functions are integrated into standard PC interface chip.
Allows many communication parameters to be programmed.

## Slide 4: Serial communication
Characters are transmitted separately:
time
bit 0
bit 1
bit n-1
no
char
start
stop
...

## Slide 5: Serial communication parameters
Baud (bit) rate.
Number of bits per character.
Parity/no parity.
Even/odd parity.
Length of stop bit (1, 1.5, 2 bits).

## Slide 6: 8251 CPU interface
CPU
8251
status
(8 bit)
data
(8 bit)
serial
port
xmit/
rcv

## Slide 7: Serial port mode bits
mode[1:0]: baud rate
  00: synchronous
  01: async, no clock prescaler
  10: async, 16x prescaler
  11: async, 64x prescaler
mode[3:2]: bits/char
  00: 5 bits
  01: 6 bits
  10: 7 bits
  11: 8 bits.
mode[5:4]: parity
  00, 10: no parity
  01: odd parity
  11: even parity
mode[7:6]: stop bit
  00: invalid
  01: 1 stop bit
  10: 1.5 stop bits
  11: 2 stop bits

## Slide 8: Serial port command register
mode[0]: transmit enable
mode[1]: set nDTR output
mode[2]: enable receiver
mode[3]: send break
mode[4]: reset error flags
mode[5]: set nRTS
mode[6]: internal reset
mode[7]: hunt mode

## Slide 9: Serial port status register
status[0]: transmitter ready
status[1]: receiver ready
status[2]: transmission complete
status[3]: parity
status[4]: overrun
status[5]: frame error
status[6]: sync char deleted
status[7]: nDSR value

## Slide 10: Programming I/O
Two types of instructions can support I/O:
  special-purpose I/O instructions;
  memory-mapped load/store instructions.
Intel x86 provides in, out instructions. Most other CPUs use memory-mapped I/O.
I/O instructions do not preclude memory-mapped I/O.

## Slide 11: ARM memory-mapped I/O
Define location for device:
DEV1 EQU 0x1000
Read/write code:
  LDR r1,#DEV1 ; set up device adrs
  LDR r0,[r1] ; read DEV1
  LDR r0,#8 ; set up value to write
  STR r0,[r1] ; write value to device

## Slide 12: SHARC memory mapped I/O
Device must be in external memory space (above 0x400000).
Use DM to control access:
  I0 = 0x400000;
  M0 = 0;
  R1 = DM(I0,M0);

## Slide 13: Peek and poke
Traditional HLL interfaces:
  int peek(char *location) {
  return *location; }
  void poke(char *location, char newval) {
  (*location) = newval; }

## Slide 14: Busy/wait output
Simplest way to program device.
  Use instructions to test when device is ready.
current_char = mystring;
while (*current_char != ‘\0’) {
poke(OUT_CHAR,*current_char);
while (peek(OUT_STATUS) != 0);
current_char++;
}

## Slide 15: Simultaneous busy/wait input and output
while (TRUE) {
/* read */
while (peek(IN_STATUS) == 0);
achar = (char)peek(IN_DATA);
/* write */
poke(OUT_DATA,achar);
poke(OUT_STATUS,1);
while (peek(OUT_STATUS) != 0);
}

## Slide 16: Interrupt I/O
Busy/wait is very inefficient.
  CPU can’t do other work while testing device.
  Hard to do simultaneous I/O.
Interrupts allow a device to change the flow of control in the CPU.
  Causes subroutine call to handle device.

## Slide 17: Interrupt interface
CPU
status
reg
data
reg
mechanism
PC
intr request
intr ack
data/address
IR

## Slide 18: Interrupt behavior
Based on subroutine call mechanism.
Interrupt forces next instruction to be a subroutine call to a predetermined location.
  Return address is saved to resume executing foreground program.

## Slide 19: Interrupt physical interface
CPU and device are connected by CPU bus.
CPU and device handshake:
  device asserts interrupt request;
  CPU asserts interrupt acknowledge when it can handle the interrupt.

## Slide 20: Example: character I/O handlers
void input_handler() {
achar = peek(IN_DATA);
gotchar = TRUE;
poke(IN_STATUS,0);
}
void output_handler() {
}

## Slide 21: Example: interrupt-driven main program
main() {
while (TRUE) {
if (gotchar) {
poke(OUT_DATA,achar);
poke(OUT_STATUS,1);
gotchar = FALSE;
}
}
}

## Slide 22: Example: interrupt I/O with buffers
Queue for characters:
head
tail
head
tail
a

## Slide 23: Buffer-based input handler
void input_handler() {
char achar;
if (full_buffer()) error = 1;
else { achar = peek(IN_DATA); add_char(achar); }
poke(IN_STATUS,0);
if (nchars == 1)
{ poke(OUT_DATA,remove_char(); poke(OUT_STATUS,1); }
}

## Slide 24: I/O sequence diagram
:foreground
:input
:output
:queue
empty
a
empty
b
bc
c

## Slide 25: Debugging interrupt code
What if you forget to change registers?
  Foreground program can exhibit mysterious bugs.
  Bugs will be hard to repeat---depend on interrupt timing.

## Slide 26: Priorities and vectors
Two mechanisms allow us to make interrupts more specific:
  Priorities determine what interrupt gets CPU first.
  Vectors determine what code is called for each type of interrupt.
Mechanisms are orthogonal: most CPUs provide both.

## Slide 27: Prioritized interrupts
CPU
device 1
device 2
device n
L1 L2 .. Ln
interrupt
acknowledge

## Slide 28: Interrupt prioritization
Masking: interrupt with priority lower than current priority is not recognized until pending interrupt is complete.
Non-maskable interrupt (NMI): highest-priority, never masked.
  Often used for power-down.

## Slide 29: Example: Prioritized I/O
:interrupts
:foreground
:A
:B
:C
B
A,B
C
A

## Slide 30: Interrupt vectors
Allow different devices to be handled by different code.
Interrupt vector table:
handler 0
handler 1
handler 2
handler 3
Interrupt
vector
table head

## Slide 31: Interrupt vector acquisition
:CPU
:device
receive
request
receive
ack
receive
vector

## Slide 32: Generic interrupt mechanism
intr?
N
Y
Assume priority selection is handled before this point.
N
ignore
Y
ack
vector?
Y
Y
N
timeout?
Y
bus error
call table[vector]
intr priority >
current priority?
continue
execution

## Slide 33: Interrupt sequence
CPU acknowledges request.
Device sends vector.
CPU calls handler.
Software processes request.
CPU restores state to foreground program.

## Slide 34: Sources of interrupt overhead
Handler execution time.
Interrupt mechanism overhead.
Register save/restore.
Pipeline-related penalties.
Cache-related penalties.

## Slide 35: ARM interrupts
ARM7 supports two types of interrupts:
  Fast interrupt requests (FIQs).
  Interrupt requests (IRQs).
Interrupt table starts at location 0.

## Slide 36: ARM interrupt procedure
CPU actions:
  Save PC. Copy CPSR to SPSR.
  Force bits in CPSR to record interrupt.
  Force PC to vector.
Handler responsibilities:
  Restore proper PC.
  Restore CPSR from SPSR.
  Clear interrupt disable flags.

## Slide 37: ARM interrupt latency
Worst-case latency to respond to interrupt is 27 cycles:
  Two cycles to synchronize external request.
  Up to 20 cycles to complete current instruction.
  Three cycles for data abort.
  Two cycles to enter interrupt handling state.

## Slide 38: C55x interrupts
Latency is between 7 and 13 cycles.
Maskable interrupt sequence:
  Interrupt flag register is set.
  Interrupt enable register is checked.
  Interrupt mask register is checked.
  Interrupt flag register is cleared.
  Appropriate registers are saved.
  INTM set to 1, DBGM set to 1, EALLOW set to 0.
  Branch to ISR.
Two styles of return: fast and slow.

## Slide 39: PIC16F interrupts
Synchronous interrupts come from inside CPU.
Asynchronous interrupts come from outside CPU.
INTCON register holds interrupt control bits.
  GIE allows unmasked interrupts.
  PIE allows peripheral interrupts.
  TMR0 enables timer 0.
  INT enables external interrupts.
  PIR1/PIR2 control peripheral interrupts.
RETFIE used to return from interrupts.
Latency:
  Synchronous: 3Tcy
  Asynchronous: 3 to 3.75 Tcy

## Slide 40: Supervisor mode
May want to provide protective barriers between programs.
  Avoid memory corruption.
Need supervisor mode to manage the various programs.
SHARC does not have a supervisor mode.

## Slide 41: ARM supervisor mode
Use SWI instruction to enter supervisor mode, similar to subroutine:
  SWI CODE_1
Sets PC to 0x08.
Argument to SWI is passed to supervisor mode code.
Saves CPSR in SPSR.

## Slide 42: Exception
Exception: internally detected error.
Exceptions are synchronous with instructions but unpredictable.
Build exception mechanism on top of interrupt mechanism.
Exceptions are usually prioritized and vectorized.

## Slide 43: Trap
Trap (software interrupt): an exception generated by an instruction.
  Call supervisor mode.
ARM uses SWI instruction for traps.
SHARC offers three levels of software interrupts.
  Called by setting bits in IRPTL register.

## Slide 44: Co-processor
Co-processor: added function unit that is called by instruction.
  Floating-point units are often structured as co-processors.
ARM allows up to 16 designer-selected co-processors.
  Floating-point co-processor uses units 1, 2.
C55x uses co-processors as well.

## Slide 45: C55x image/video hardware extensions
Available in 5509 and 5510.
  Equivalent C-callable functions for other devices.
Available extensions:
  DCT/IDCT.
  Pixel interpolation
  Motion estimation.

## Slide 46: DCT/IDCT
2-D DCT/IDCT is computed from two 1-D DCT/IDCT.
  Put data in different banks to maximize throughput.
block
Column
DCT
interim
DCT
Row DCT

## Slide 47: C55 DCT/IDCT coprocessor extensions
Load, compute, transfer to accumulators:
  ACy=copr(k8,ACx,Xmem,Ymem)
Compute, transfer, mem write:
  ACy=copr(k8,ACx,ACy), Lmem=ACz
Special:
  ACy=copr(k8,ACx,ACy)

## Slide 48: Software pipelined load/compute/store for DCT
Iteration i-1
Dual_load
8
compute
4
Long_store
4 empty
3
Dual_load
empty
Iteration i
Dual_load
8
compute
4
Long_store
4 empty
3
Dual_load
empty
Iteration i+1
Dual_load
8
compute
4
Long_store
4 empty
3
Dual_load
empty
op_i(0), load_i+1(0,1)
op_i(1), store_i-1(0,1)
op_i(2), store_i-1(2,3)
op_i(2), store_i-1(4,5)
op_i(2), store_i-1(6,7)
op_i(2), load_i+1(2,3)
…

## Slide 49: C55 motion estimation
Search strategy:
  Full vs. non-full.
Accuracy:
  Full-pixel vs. half-pixel.
Number of returned motion vectors:
  1 (one 16x16) vs. 4 (four 8x8).
Algorithms:
  3-step algorithm (distance 4,2,1).
  4-step algorithm (distance 8,4,2,1).
  4-step with half-pixel refinement.

## Slide 50: Four-step motion estimation breakdown
d = {8,4,2,1};
for (i=0; i<4; i++) {
compute 3 upper differences for d[i];
compute 3 middle differences for d[i];
compute 3 lower differences for d[i];
compute minimum value;
move to next d;
}
X

## Slide 51: C55 motion estimation accelerator
Includes 3 16-bit pixel data paths, 3 16-bit absolute differences (ADs).
Basic operation:
  [ACx,ACy] = copr(k8,ACx,ACy,Xmem,Ymem,Coeff)
  K8 = control bits (enable AD units, etc.)
  ACx, ACy = accumulated absolute differences
  Xmem, Ymem = pointers to odd, even lines of the search window
  Pointer to two adjacent pixels from reference window

## Slide 52: C55 pixel interpolation
Given four pixels A, B, C, D, interpolate three half-pixels:
A
B
C
D
U
M
R

## Slide 53: Pixel interpolation coprocessor operations
Load pixels and compute:
  ACy=copr(k8,AC,Lmem)
Load pixels, compute, and store:
  ACy=copr(k8,AACx,Lmem) || Lmem=ACz